## Slide 1: SpindleUtil Manual
By T47, Dec 2014

## Slide 2: Contens
Introduction
Image Processing
  Input Arguments
  Interactive Interface: Define Spindle from Image
  Output Plots
Data Processing
  Ratio Calculation
  MATLAB Data Structure
Function Usages

## Slide 3: Introduction
SpindleUtil is a set of MATLAB scripts to facilitate the process of spindle line-scan quantitation. It is aimed to improve the productivity by replacing the “traditional” way of manually draw lines in MetaMorph and process data by hand using Excel.
SpindleUtil makes it much easier in rotating the image to position poles vertically. It also introduces box-scan, as well as the line-scan as a comparison.
SpindleUtil automates the quantitation, data visualization, comparison, and data management, making it all done in MATLAB.

## Slide 4: Introduction
In this manual, we will demonstrate the basic setup and process. Using a test dataset, the interface and output files will be illustrated.
For future expansions, the steps after the FITC/TexRd ratio plot needs to be developed and tested.
All scripts are named with “spindle_” prefix, making it easier to identify in MATLAB
You should “Set Path” first to include those scripts.

## Slide 5: Without SpindleUtil
Before SpindleUtil became available, the image quantitation is done with MetaMorph and Excel. Lines are drawn in MetaMorph, suffering problems with inconsistent spindle boundaries. Data was exported to a huge Excel sheet, making plots and comparisons are thus hard and cumbersome.
Line-scan Plots
Quantitation Comparison

## Slide 6: With SpindleUtil
SpindleUtil aims to take over the whole process using MATLAB, eliminating the complicated and time-consuming data transfer.
SpindleUtil takes advantage of an interactive interface for spindle rotation and boundary setup, which is faster than in MetaMorph or ImageJ.
SpindleUtil quantitates the intensity from the original TIFF, and overlays them to each other using normalized inter-pole distance. This is much faster than Excel.
SpindleUtil automatically saves all figures, log, and workspace data to an “analysis” folder in an organized way.

## Slide 7: Box-scan Quantitation
One advantage of using SpindleUtil is its box-scan quantitation, especially when comes to deformed spindle geometry, e.g. splayed poles.
Line-scan quantitation only takes account for the center line (pole-pole line) and 2 side-lines. This is representative in regular spindles, but may be inaccurate and losing information.
Box-scan draws as many lines as possible in the spindle (including the 3 lines in line-scan), and thus averaging the whole spindle. This is useful in e.g. splayed pole case where the pole is not focused.

## Slide 8: Section 1: Image Processing
In this section, we will go over the pipeline of image processing, which is from raw TIFF files to quantitated traces saved in MATLAB session.
Related scripts are in folder:
Scripts/SpindleQuantify/ImageProcess
However, you will be using a master function spindle_mat_analysis, instead of any individual functions in the above folder.

## Slide 9: spindle_mat_analysis
This is an all-in-one function to perform the analysis pipeline.
Usage: spindle_mat_analysis (dir_name, CEN_LINE_OFFSET, POLE_PORTION)
Arguments:
  dir_name: (type string), the name of the folder containing all the TIFF images.
  CEN_LINE_OFFSET: (type int), the distance between side-lines and the center line used in line-scan. If not specified, default of 5 will be used.
  POLE_PORTION: (type float), the portion along the pole-pole axis considered as pole region. If not specified, default of 1/24 will be used.

## Slide 10: More about the arguments
dir_name:
  First, make sure your “current working directory” is correct (see left panel in MATLAB window). Go to the parent directory of your image-file folder (so that the target folder is a child of the current working directory).
  Second, use the target directory name as dir_name. For example, “3. M+F2MCAK” (exactly as is, including whitespaces).

## Slide 11: More about the arguments
dir_name:
  All TIFF files should meet the format of “Prefix_XXX_fluroChannel.TIF”:
    Prefix should be exactly same as the parent folder name (i.e. dir_name).
    ID number is 3-digit, (filled with 0s). It needs to be neither continuous (of files in the same folder), nor starting with 001.
    Fluorophore Channel should be one of the following: “w1DAPI”, “w2FITC”, “w3Texas Red”. This is same as default by microscope image output.
    Extension is “TIF”, not “TIFF”.
    Valid image name example:
    “3. M+F2MCAK_001_w2FITC.TIF”.
  “nd” and “_thumb” files in the folder will be ignored.

## Slide 12: More about the arguments
dir_name:
  The script is expecting that for each spindle (set), 3 images of each channel are present. Thus, the number of total legit TIF images should be multiples of 3.
  Possible error messages:
  ERROR: directory not found.
  ERROR: TIFF images set (of 3) incomplete.
  14 non-thumb TIF files present.
  ERROR: TIF and directory name mismatch.
  3. M+F2MCAK/5. M+715AA_001_w1DAPI.TIF

## Slide 13: More about the arguments
CEN_LINE_OFFSET:
  This defines the distance between the 3 lines used in line-scan. In line-scan, one center line is drawn, and two side-lines (one on each side) CEN_LINE_OFFSET pixels away are automatically drawn.
  Default is 5 (pixels), as inherited from older MetaMorph approaches.

## Slide 14: More about the arguments
POLE_PORTION:
  This defines the portion of spindle considered as “pole region”. Default is 1/24, which means the inter-pole distance will be divided to 24 sections, where the 1st and 24th section are considered “north” and “south” pole, while the 2nd-to-23rd sections are “body”.
  This number is useful when comparing a distribution of “pole” (where MTs are enriched) to rest of spindle. Currently, no calculation in the output files is dependent on this argument. But it can be used in marking the boundary on plots.
  Use 1/24, not 24.

## Slide 15: spindle_mat_analysis
A successful launch will show the following message in MATLAB console:
Load files from directory: 3. M+FMCAK
Load 15 non-thumb TIF images from directory.
Group into 5 spindles {DAPI, FITC, TexRd}.
Instructions:
First rotate image to where poles are aligned vertically (north-south),
then draw box to encompass full spindle
(two horizontal, two vertical, one vertical center line).
Controls:
Keys: up/left: counterclockwise 1°/5°; down/right: clockwise 1°/5°;
r: reset; p: pass; q: save & next;
x: abort (premature terminate, data lost).
Lines: 1/2: horizontal (top / bottom boundary);
3/4: vertical (left / right boundary);
5: vertical (linescan center).

## Slide 16: Define spindle from image
For each spindle set (of 3 images representing each channel), we will select a region that defines the spindle. This is done using an interactive interface.
A window will pop out (see next page), with a cross-cursor and key descriptions.
We will first rotate the image, then draw 5 lines to define the spindle.

## Slide 17: Interactive interface

## Slide 18: Rotate the spindle
This is to make the line drawing easier. The goal is to rotate the image so that the spindle is oriented/aligned north-to-south (vertical).
To do so, use the following control keys:
  Up: rotate counterclockwise by 1 degree;
  Down: rotate clockwise by 1 degree;
  Left: rotate counterclockwise by 5 degree;
  Right: rotate clockwise by 5 degree.
Use left/right first to rotate the image, then refine by up/down. You can check the orientation by overlaying the cursor, which has vertical cross-line.
The current rotation angle is shown in bottom-left corner (cyan).

## Slide 19: Interactive interface

## Slide 20: Draw 2 horizontal lines
These first 2 lines are horizontal and defines the north and south boundary. They are shown in magenta. It should be drawn exactly at the outer tip of the pole (names y1 and y2).
The POLE_PORTION defined pole region will be automatically shown by dashed lines inside the 2 horizontal lines you drawn.

## Slide 21: Draw 3 vertical lines
These next 2 lines are vertical and defines the left and right boundary. They are shown in cyan. It should be drawn exactly at the widest point of the spindle (named x1 and x2).
The last vertical line mimics the line-scan, where it should be through both poles. So it’s not necessarily at the center. It is shown in yellow (named x0), and the CEN_LINE_OFFSET defined two side-lines are shown in dashed lines.

## Slide 22: Interactive interface

## Slide 23: Interactive interface
At this point, the line drawing is complete. Hit “q” to save and quit, which leads you to the next spindle.
Other keys:
  r: reset, restores the original image and erases all lines;
  p: pass, the current spindle is considered bad (quality), thus it will be excluded from the following analysis (does not count in ratio calculation); Any rotation or lines drawn will be ignored.
  x: abort: quit the spindle_mat_analysis function without saving any data (all will be lost).

## Slide 24: Interactive interface
Note:
  The “close window” button is disabled to avoid mistaken clicks. Neither does “command+w” works.
  The MATLAB console window may gain focus when you click keys too fast. Use “command+`” to switch back to it.
  You can’t go back to a spindle once “q” or “p”. So think twice before passing/finishing a spindle.

## Slide 25: Spindle output
Once you’ve done the definition for all spindles in the folder, an output file (.eps) will be saved for each spindle. See example next page.
The output file includes the image of the spindle (rotated), the 5 lines drawn on top of the image, parameters used, and the quantitated traces. Although printing out the output is costly (color printing, black background), it is a good record.
Outputs are saved to “Prefix_analysis/summary” with same name as spindle, e.g. “3. M+F2MCAK_summary/summary/3. M+F2MCAK_002.eps” (not same folder as TIF data).

## Slide 26: Output file

## Slide 27: Spindle output
First 2 plots are the fluorescence intensity from pole-to-pole, averaged by box-scan and line-scan, respectively.
X-axis is the pole length in pixels; Y-axis is the averaged fluorescence. Again, box-scan averaged all columns while line-scan only samples 3 columns.
The 3rd plot is the FITC/TexRd ratio (assuming that FITC channel is protein of interest and Texas Red is labeled MTs). Ratio at each pixel position is calculated by dividing the FITC intensity by TexRd. X-axis is normalized to 0%-to-100% and the POLE_PORTION line is drawn for reference.

## Slide 28: Section 2: Data Processing
In this section, we will go over the pipeline of data processing, which is from quantitated traces to normalized FITC/TexRd ratio.
Related scripts are in folder:
Scripts/SpindleQuantify/DataProcess
However, you will still be using a master function spindle_mat_analysis, instead of any individual functions in the above folder (continuously from section 1).

## Slide 29: Calculating the ratio
As described in the previous section, FITC/TexRd ratio of each spindle is calculated by simple division.
However, the ratio of each spindle cannot be averaged directly since the length of each spindle (pole-to-pole distance in pixels) are different, thus the number of points in the (0%-to-100%) range is different.
To solve the problem, we group the data points in the ratio trace to 100 bins first, then average the binned ratio trace across spindles.
This is done by spindle_mat_average_ratio function, with a default NUM_BIN = 100.

## Slide 30: Calculating the ratio
Briefly, the grouping into bins is simple:
  Divide 0%-100% into 100 bins (1% each);
  Find the data points in the original ratio in each bin;
  Assign ratio of each (1%) bin by averaging the ratio data points fall in the bin.
Usually, the pole-to-pole distance in pixels is larger than 100. So each 1% bin will have at least one ratio data points.
In the end, an average of ratio of all spindles is calculated and plotted (as well as standard deviation).

## Slide 31: Calculating the ratio
An example output is in next page.
For box-scan and line-scan, the averaged ratio (across spindles) is colored in black and overlaid to all individual ratio traces.
The averaged ratio is plotted against each other (box-scan vs. line-scan) with error bars.
Overall, the box-scan and line-scan agrees in trends, while box-scan has smaller errors.

## Slide 32: Ratio

## Slide 33: Calculating the ratio
Notes: